## Slide 1: Rover Assembly
Jackson State University

## Slide 2: Rover Assembly
Jackson State University

## Slide 3: Assembled Rover
Wheels/Motors
Power
Switch
BT Radio
Arduino UNO
Driver Board
Platform
Motor
Side
Brackets

## Slide 4: Getting Started
Best to have a convenient worktable …
Work surface large enough to accommodate Assembly Guide, parts & tools
Towel as a soft “work-area” mat (Keep parts from falling on floor!)
Tools needed – Phillips's screwdriver & needle nose pliers
Rover Fastener Parts package – screws, nuts, & 4-spacers
Rover parts – platform, 2-motor side brackets, 4-wheels, 4-motors, & battery tray
Electrical – Power switch, wire harness, Arduino UNO, motor driver board, & battery holder
Where to start?

## Slide 5: Parts Layout
Long
Screws
Flat Head
Screws
Arduino
Screws
Motor Side
Brackets
Battery Holder
Battery Tray
Rover
Platform
Wheels
Motors
Arduino
Motor Driver
Board
Fasteners

## Slide 6: Attaching Motor Side Brackets
What’s needed…
Motor Side Bracket, 4 – ½ inch FLAT HEAD screws, 4 – nuts
Phillip’s screwdriver and needle nose pliers
Note orientation of bracket – mounting flange toward middle of platform Do not over-tighten screws!

## Slide 7: Attach Side Bracket
How to…
Insert flathead screw through platform & bracket
Screw nut on threads with fingers
Tighten lightly
Insert second screw & remaining screws

## Slide 8: Attach other Side Bracket
Both motor side brackets are the same
Use remaining two FLAT head screws & nuts to attach other side bracket
Flange faces to center of platform
Tighten securely but do not over tightened

## Slide 9: Attach Arduino UNO Board
Add remaining three screws, nuts & tighten lightly with HEX wrench…
Place socket screw through Arduino mounting hole with spacer on bottom
Place socket screw through platform mounting hole with spacer & nut on bottom side

## Slide 10: Install Rover Drive Motors
What’s needed…
Two drive motor pairs , 8 – long screws (1-1/4 inch), 8 – nuts
Phillip’s screwdriver & needle nose pliers
Notes…
Each motor pair is mounted on the same side of the Rover side bracket
Motors are mounted with wires facing outward
Place 2 – screws through motor mounting holes – align with bracket – attach nuts on backside of motor bracket

## Slide 11: Mounting Drive Motors
What to do…
  Attach 4-drive motors
  Use 8-long screws (1-1/4 in) & nuts
  Motor wires face outward as shown
  Tighten with Phillip’s screwdriver and pliers
  Do not overtighten
Long Screws

## Slide 12: Attach Wheels
Note the shape of the
Axle hole in the wheel hub – Flat sides must align with motor axle!
Align wheel & axle and press together – may have to rotate wheel slightly – index fingers must support back side of motor and bracket

## Slide 13: Install Power Switch
Parts
Small screws
Washers
Switch
Nuts
What to do…
Install power switch
Screws & washers on top
Switch and nuts on bottom

## Slide 14: Summary
What we did…
  Check and review Rover part names
  Follow assembly steps…
  Assemble Side brackets to platform – left & right
  Install Arduino with socket screws & spacers to platform
  Attach driver 2 driver motor pairs – wires face out
  Attach 4 wheels – note “flats” on axle and wheel hubs – align & press on with fingers
  Install power switch with small screws, washers & nuts

## Slide 15: Resources
Arduino Smart Car/Robots photos
Arduino RADAR
Prosthetic Hand
Egg Incubator
How Tall Are You? (Measure person’s height)
Binary Counter
AI & Machine Learning for Kids (Middle School)
Transformer's Baby: Arduino Avoiding Obstacle Robot
Search for High School Arduino Sensor Projects
Use SHIFT-click